## Slide 1: Parkinson's Continuity-of-Care Platform
CONTINUITY OF CARE
Turning passive tremor and fall data into medication-aware, personalized follow-up and early escalation to the care team
Medication-aware
Personalized
Early escalation

## Slide 2: Continuity of care, not just monitoring
THE PITCH
A continuity-of-care platform that turns passive tremor and fall data into medication-aware, personalized follow-up and early escalation to the care team.
Medication-aware
Personalized
Early escalation

## Slide 3: Care Breaks Down Between Visits
THE PROBLEM
Visits Are Rare, Symptoms Aren't
Patients see a neurologist every few months, but tremor and mobility shift daily. Most of the disease course goes unseen.
Medication Timing Is Hard to Tune
Levodopa response varies through the day. Without between-visit data, adjusting dose timing is largely guesswork.
Falls and Gaps Surface Late
Balance problems raise fall risk, and missed doses or overdue follow-ups often show up only after a crisis.
10M+
People living with Parkinson's disease worldwide
75%
Experience tremor as a primary symptom
2–3x
Higher fall rate than healthy older adults
The need: a continuity-of-care platform that connects daily symptoms, medication and follow-up, and flags concerns to the care team early.

## Slide 4: One Platform, Four Connected Functions
SOLUTION
Sense
Passive tremor and fall detection plus quick daily check-ins.
Coordinate
Medication schedules, adherence logs and dose-linked symptom trends.
Personalize
A care plan adapted to living situation, caregiver support and mobility.
Escalate
Predefined warning signs sent to clinicians for review.
How it works
1
Capture
Tremor, falls and quick check-ins are collected passively and by simple patient input.
2
Interpret
Data is linked to medication timing, the care plan and appointments to reveal patterns.
3
Act
Predefined warning signs reach the care team for review, with weekly summaries.

## Slide 5: Passive Tremor and Fall Sensing Feeds the Platform
DATA SOURCE
Tremor analysis
1
Capture: Motion signal is split into short analysis windows.
2
Transform: A Hamming window and FFT convert each window to a frequency spectrum.
3
Measure: Energy in the 3.5–7 Hz band is tracked (typical PD rest tremor: 4–6 Hz).
4
Score: A timestamped severity score is logged for trends and dose linkage.
Fall detection
1
Idle: Motion magnitude is monitored; free-fall is flagged below 0.35g.
2
Free-fall: Within 100–500 ms, an impact above 2.5g and rotation above 120°/s is checked.
3
Confirm: A 3-second confirmation window limits false alarms.
4
Log and escalate: Confirmed falls are recorded and sent as an urgent alert.
These signals are the data source. The product is what the platform does with them.

## Slide 6: Medication Coordination: Linking Doses to Symptoms
KEY DIFFERENTIATOR
Chart: Tremor severity by hours since dose (illustrative)
| 0h | 1h | 2h | 3h | 4h | 5h
Tremor severity | 18 | 14 | 22 | 48 | 63 | 70
Schedules and reminders
Dose times set with the care team.
Adherence logging
Taken, late and missed doses recorded.
Dose–tremor correlation
Symptom patterns shown against dose timing.
Clinician insight: “Tremor rises about 3 hours after the morning dose on most days this week.”

## Slide 7: Daily Check-ins and a Personalized Care Plan
PERSONALIZATION
Quick patient-reported check-ins
Mood
Sleep
Stiffness
On / off periods
Takes under a minute. Answers feed the clinician summary and the risk logic.
Care plan adapted to the patient
Doctor's instructions
Neurologist's plan turned into clear daily steps.
Lives alone
Stronger fall escalation and proactive check-ins.
Caregiver available
Tasks and alerts shared with the right person.
Limited mobility
Remote follow-up favored over travel.

## Slide 8: Follow-up Gap Detection and Early Risk Flags
PROACTIVE LOGIC
Follow-up gap detection
Visit tracking
Neurologist visits and recommended tests tracked per patient.
Overdue detection
Tests and reviews past due are flagged to the care team.
Missed appointments
Detected automatically, with a prompt to rebook.
Predicting a difficult week
Rising tremor trend
Missed levodopa doses
More “off” time reported
High-risk week
Early review by the care team
Beyond reminders: rules adapt to each patient's own baseline, so alerts reflect change rather than fixed averages.

## Slide 9: Early Escalation of Predefined Warning Signs
ESCALATION
Warning sign | Priority | Who is notified | Next step
Confirmed fall | Urgent | Caregiver and care team | Immediate alert, then clinician review
Sharp rise in tremor severity | High | Care team | Flagged for clinician review
Repeated missed doses | High | Patient and caregiver; care team if it persists | Reminder first, then review
Missed or overdue follow-up | Routine | Care team | Outreach prompt to reschedule
More “off” time or poor check-ins | Routine | Care team | Included in weekly summary and review
Alerts go to clinicians for review. The platform does not diagnose, give treatment advice or replace clinical judgment.

## Slide 10: Care-Team Dashboard: Clinician and Caregiver Views
CARE TEAM
Clinician view: weekly summary (sample data)
1
Falls this week
+18%
Tremor vs last week
86%
Dose adherence
Overdue
Next follow-up
Chart: Daily tremor severity index
| Mon | Tue | Wed | Thu | Fri | Sat | Sun
Tremor severity | 32 | 35 | 31 | 44 | 52 | 58 | 61
Caregiver view
Today's doses
Taken, late or missed.
Fall alerts
Instant, with timestamp.
Tasks and visits
What is due and when.
Check-in summary
Mood, sleep and stiffness.

## Slide 11: Authorized Access and Clinical Safeguards
TRUST
Role | Can see | Can do
Patient | Own data, care plan and check-ins | Log doses and symptoms; grant or revoke consent
Caregiver | Shared alerts and tasks, with consent | Acknowledge alerts and support tasks
Neurologist | Full trends, summaries and alerts | Review alerts and update the care plan
Nurse or coordinator | Follow-up status, adherence and alerts | Reach out and reschedule visits
Consent first
Patients choose who sees their data.
Role-based access
Each role sees only what it needs.
Review, not diagnosis
Clinicians decide; the platform informs.

## Slide 12: Benefits for Patients, Caregivers and Clinicians
IMPACT
Patients
Safer at home, with fast fall escalation
A simple plan that fits daily life
Fewer missed doses and follow-ups
Caregivers
Shared alerts without constant checking
Clear tasks and appointment reminders
Confidence that concerns reach the clinic
Care team
Visibility into symptoms between visits
Medication-aware trends before each visit
Prioritized alerts and weekly summaries
Outcome: fewer blind spots between visits, earlier action, and more focused consultations.